## Slide 1: Securing Automotive Networks against the Quantum Threat
Post-Quantum Cryptography in UDS 0x29 Architecture

## Slide 2: The Quantum Threat
Current automotive security relies heavily on RSA and ECC (Elliptic Curve Cryptography).
In 1994, Peter Shor proved mathematically that a large Quantum Computer can break these algorithms exponentially faster.
When Cryptographically Relevant Quantum Computers (CRQCs) arrive, ECC and RSA will offer zero security.
Given 10-15 year vehicle lifespans, ECUs designed today are already at risk.

## Slide 3: QKD vs PQC in Automotive
Quantum Key Distribution (QKD) uses quantum mechanics (entangled photons) to secure keys.
Why it fails for automotive:
- Requires pristine fiber-optic cables, dedicated lasers, and expensive hardware.
- Impossible to run over copper CAN buses.
- Cannot provide digital signatures for OTA firmware updates.
The mandated NIST Solution: Post-Quantum Cryptography (PQC).

## Slide 4: The PQC Solution
PQC relies on complex new mathematics (like Lattice-based crypto) resistant to quantum algorithms.
No quantum hardware needed — runs entirely on standard classic microcontrollers (e.g., STM32).
NIST Standardized Algorithms:
- ML-DSA (Dilithium) for Digital Signatures (Authentication & OTA).
- ML-KEM (Kyber) for Key Encapsulation (Secure Sessions).
The Engineering Challenge: PQC keys and signatures are 10x to 50x larger than classical ECC keys.

## Slide 5: Project Overview & Execution Phases
Phase 1: Automotive Transport Baseline (Overcome 8-byte CAN limits for 15KB data).
Phase 2: Crypto Abstraction Layer (CAL) (Decouple UDS logic from cryptography).
Phase 3: Classical UDS 0x29 State Machine (Establish timing and memory baselines).
Phase 4: Post-Quantum Integration (Swap Classical for ML-DSA and ML-KEM).
Phase 5: Hybrid Mode & GUI Demonstration (TouchGFX visual hot-swapping).

## Slide 6: Current Advancements & State
Transport Layer (Done): ISO-TP extended framing successfully moves 15.3 KB of data over FDCAN.
Crypto Abstraction Layer (CAL) (Done): Vtable architecture actively wrapping mbedTLS (X.509, ECDH, AES-256-GCM).
UDS 0x29 State Machine (Complete):
- Zero-Copy memory overlays implemented (saving ~4KB RAM).
- Asynchronous NRC 0x78 (Response Pending) flow implemented natively to prevent 50ms P2 timeouts during slow crypto math operations.

## Slide 7: Immediate Next Steps
Physical Hardware Deployment:
Flash the completed Transport, CAL, and UDS binaries onto the twin STM32H7 evaluation boards.
Test the Classical UDS 0x29 Authentication flow over live FDCAN.
Profile the runtime execution speed and memory consumption.
Validate that NRC 0x78 pending timeouts successfully hold the diagnostic channel open.
Once classical baseline is validated, integrate PQClean (ML-DSA) into the CAL Vtable.